## Slide 1: ELEC1200: A System View of Communications: from Signals to Packets Lecture 12
Motivation
  Music as a combination of sounds at different frequencies
Cosine waves
  Continuous time
  Discrete time
Decomposing signals into a sum of cosines
  Amplitude Spectrum

## Slide 2: Motivation: Music
Music is a combination of sounds with different frequencies:
In this lecture, we see that this is true of any waveform
0
5
10
15
20
25
30
-1
0
1
frequency = 261.63Hz (C4)
0
5
10
15
20
25
30
-1
0
1
frequency = 329.63Hz (E4)
0
5
10
15
20
25
30
-1
0
1
frequency = 392.00Hz (G4)
0
5
10
15
20
25
30
-1
0
1
combination
time in milliseconds
increasing frequency

## Slide 3: Visualizing the frequency content of music
Windows Media Player
Right click->Visualizations->Bars and Waves->Bars
frequency
amplitude

## Slide 4: Sinusoidal Waves
Cosine Wave Sine Wave
Parameters:
= period (in seconds)
= frequency in hertz (cycles per second)
= frequency in radians per second
-2
-1
0
1
2
t (sec)
x(t)
-2
-1
0
1
2
t (sec)
x(t)

## Slide 5: We only need cosines
A sine wave is just a cosine with a phase shift of
A negative phase shift introduces a delay of
0
-1
0
1
0
-1
0
1
0
-1
0
1
0
-1
0
1
0
-1
0
1
delay

## Slide 6: General Form
Any sinusiodal signal can be expressed as

## Slide 7: Discrete Time Cosines
Consider a discrete time cosine waveform with N samples:
In the following, we assume N is even.
If we have only N samples, it turns out that we only need to consider N/2+1 frequencies:
For all N, it is always true that 0 ≤ fk ≤ 0.5
k indicates how many times the cosine repeats in N samples
The larger k, the higher the frequency
Different waveforms are obtained by changing the parameters Ak and qk in the equation
fk is called a normalized frequency
It has units of cycles/sample

## Slide 8: Discrete time cosines with varying fk
0
10
20
30
40
50
60
-1
0
1
f1 = 1/64
-1
0
1
f2 = 2/64
-1
0
1
f4 = 4/64
-1
0
1
f8 = 8/64
0
10
20
30
40
50
60
0
10
20
30
40
50
60
0
10
20
30
40
50
60
n

## Slide 9: Normalized vs continuous frequency
Given a continuous cosine of frequency and sampling at frequency Fs, we get a set of samples x(n):
Units of f are cycles per sample:
Conversion:
0
3/6
1
1.5
2
-1
0
1
= 1Hz cosine sampled at Fs = 6Hz
time in seconds
Ts
0
1
2
3
4
5
6
7
8
9
10
11
12
1/6
2/6
sample index
4/6
5/6
frequency in Hz
normalized frequency

## Slide 10: Sinusoidal Representation of Sampled Data
Any sampled data waveform x(n) with N samples:
can be expressed as the the sum of a N/2+1 cosine waves with frequencies
using the equation
This equation is called the Fourier series expansion of x(n)
Different waveforms are obtained by changing the values of Ak and fk
each term in the
summation is called a
frequency component

## Slide 11: Interpretation of
Ak controls the amplitude of the cosine with frequency fk.
k controls the phase of the cosine with frequency fk.
0
50
100
150
200
250
0
1
2
0
50
100
150
200
250
0
1
2
large low
frequency
component,
small high
frequency
component
small low
frequency
component,
large, high
frequency
component

## Slide 12: Amplitude, Phase and Frequency
Amplitude Ak
  tells us how much of each frequency there is.
  A0 controls the average level of the signal and is sometimes called the DC component.
Phase k
  Not so important, just shifts each cosine left or right.
Frequency fk
  tells us about how quickly the signal changes
  Low frequencies (small k) indicate slow changes.
  High frequencies (large k) indicate fast changes.
We are most interested in the amplitude and how it changes with k.
  The frequency components with the largest amplitude are the “most important.”

## Slide 13: Amplitude Spectrum
A plot of Ak versus k
Gives a graphical representation of which frequencies are most important

## Slide 14: Example: Square Wave
0
16
32
48
64
-1
0
1
0
8
16
24
32
0
0.5
1
1.5
0
16
32
48
64
-1
0
1
0
8
16
24
32
0
0.5
1
1.5
0
16
32
48
64
-1
0
1
0
8
16
24
32
0
0.5
1
1.5
Amplitude Spectrum
Waveform
n
k
x(n)
A2cos(2pf2n+f2)
x(n)
A2cos(2pf2n+f2)
+A6cos(2pf6n+f6)
x(n)
A2cos(2pf2n+f2)
+A4cos(2pf4n+f4)
+A10cos(2pf10n+f10)

## Slide 15: More Complex Example
0
50
100
150
200
250
-1
0
1
signal
n
0
20
40
60
80
100
120
0
0.1
0.2
amplitude spectrum
k

## Slide 16: Transforms
The Fourier Series is only one of a set of representations (transforms) you will study later:
  Fourier Transform
  Laplace Transform
  Z Transform
Transforms are merely a different way of expressing the same data. No information is lost or gained when taking a transform.
  Loose analogy: transform ~ translation
We use transforms because
  It gives us a different way of viewing or understanding the signal.
  Some operations on signals are easier to understand/analyze after taking the transform.

## Slide 17: Summary
Any signal can be expressed as the sum of cosines with different frequencies.
Cosines in discrete time use normalized frequency, which has units of cycles/sample
The amplitude spectrum
  Is the weightings (sizes) of the different frequency components, Ak, plotted as a function of k
  Tells us important information about what the signal looks like.
  Frequency components with the largest amplitudes are the “most important”
Knowledge of both the amplitude and phase spectrum is equivalent to knowledge of the signal.

## Slide 18: Appendix: Discrete Fourier Transform (DFT)
The DFT takes a waveform x(n) and returns a set of N complex valued coefficients, called Fourier coefficients.
  The Fourier coefficients are denoted by Xk for k=0,1…(N-1)
  The formula (not important for this course) is
  For this course, we use MATLAB’s “fft” function to compute the Fourier coefficients.
From the first N/2+1 Fourier coefficients, we can compute Ak and k for k=0,1,…(N/2)
This is the complex exponential
For more details wait until you take ELEC2100

## Slide 19: Appendix: complex numbers
Define
A complex number is given by z = a+jb, where
  a is the “real” part = Re{z}
  b is the “imaginary” part = Im{z}
Since a complex number has two parts, we can represent it as a point on a 2D plane (the complex plane)
By analogy with polar coordinates, we can define the magnitude and phase.
a
b
Im z
Re z

## Slide 20: Appendix: The DFT in MATLAB
The MATLAB function “fft” implements the “Fast Fourier Transform,” a fast way to compute the DFT.
>> Xdft = fft(x);
returns an N dimensional vector containing the DFT coefficients.
We need to be a bit careful with MATLAB’s indexing
  The first index of x(n) in our notation is n=0, but the first index of a vector in MATLAB starts with 1.
  Thus, if we represent a waveform x(n) for n=0,..(N-1) in a MATLAB vector x. Then,
  x(1)= x(0), x(2)= x(1),…, x(N)= x(N-1)
  Similarly,
  Xdft(1) = X0
MATLAB
signal