## Slide 1: ELEC1200: A System View of Communications: from Signals to Packets Lecture 14
Time-Frequency Analysis
  Analyzing sounds as a sequence of frames
  Spectrogram
Lossy Encoding
  MP3 encoding

## Slide 2: Time-Frequency Analysis
For many complex signals (like speech, music and other sounds), short segments are well described by a sinusoidal representation with a few important frequency components, but long segments are not.
Time-frequency analysis refers to the analysis of how short-term frequency content changes over time.
The spectrogram of a signal is a picture of how its amplitude spectrum of a signal changes over time.
  The vertical axis represents frequency
  The horizontal axis represents time
  The image color represents Fourier amplitude
    red = large amplitude, blue = small amplitude

## Slide 3: Spectrogram Example
frame number
frequency (Hz)
5
10
15
20
25
30
35
0
500
1000
1500
2000
2500
3000
3500
4000
loud
high frequency
0
1000
2000
3000
4000
0
5
10
15
20
25
30
35
frequency (Hz)
amplitude spectrum
quiet
lower frequency
0
1000
2000
3000
4000
0
5
10
15
20
25
30
35
frequency (Hz)
amplitude spectrum
loud
many frequencies
0
1000
2000
3000
4000
0
5
10
15
20
25
30
35
frequency (Hz)
amplitude spectrum
blue = quiet
red = loud

## Slide 4: Computation of the Spectrogram
Divide the signal into a set of frames, typically about 20-50ms long.
Compute the amplitude spectrum of each frame.
This gives you a two dimensional array of real numbers, indexed by frame number and frequency index.
Plot this as an image.
  It is generally more informative to plot the logarithm of the amplitude, as this compresses large amplitudes allowing the smaller details to show up.
  To avoid problems at zero, apply a small positive floor to the values (i.e. replace each amplitude by P if it is smaller than P, where P is small).
frame

## Slide 5: Speech Spectrogram
spectrogram of “she”
frame number
frequency (Hz)
5
10
15
20
25
30
35
0
500
1000
1500
2000
2500
3000
3500
4000
can you guess what word this is?
frame number
frequency (Hz)
5
10
15
20
25
30
35
0
500
1000
1500
2000
2500
3000
3500
4000

## Slide 6: Train Whistle vs. Bird Chirps
Can you figure out which is which?
spectrogram
frame number
frequency (Hz)
10
20
30
40
50
0
500
1000
1500
2000
2500
3000
3500
4000
spectrogram
frame number
frequency (Hz)
10
20
30
40
50
0
500
1000
1500
2000
2500
3000
3500
4000

## Slide 7: Speech Data
Characteristics
  Recent measurements more informative in predicting the future than those in the distant past.
  At each point in time, different sounds (phonemes) may be pronounced.
  Different phonemes have different spectral content.
red = high energy
blue = low energy
phonemes

## Slide 8: Encoding and Decoding
Encoding
  Auditory signal (from a recording) is coded into an mp3 file containing carefully stored spectral information
Decoding
  mp3 file is turned back into an auditory file that can be output to your speakers
Source
Encoding
Source
Decoding
Store/Retrieve
Transmit/Receive
bitsIN
bitsOUT

## Slide 9: Lossless vs. Lossy Compression
For lossless data compression: bitsOUT = bitsIN
  We can reconstruct the original bit stream exactly
  bitsOUT = bitsIN
  Usually used for “naturally digital” bit streams, e.g. documents, messages, datasets, …
  Examples: Huffman encoding, LZW, zip files, rar files
For lossy encodings: bitsOUT ≈ bitsIN
  “Essential” information preserved
  Appropriate for sampled data streams (audio, video) intended for human consumption via imperfect sensors (ears, eyes).
Source
Encoding
Source
Decoding
Store/Retrieve
Transmit/Receive
bitsIN
bitsOUT

## Slide 10: MP3
MPEG is moving pictures experts group
  set up by ISO (international standards organization)
  every few years issues a standard
    MPEG1 (1992)
    MPEG2(1994)..
MP3 stands for MPEG audio layer III
MP3 achieves a 10:1 compression ratio!
This enables
  bit-streaming
  compact audio storage

## Slide 11: Bad ways to compress an audio file
Reduce the total number of bits per sample
  e.g. 32 bit to 16 or 16 to 8 bit
  Gives you a factor of 2 in compression
  However, perceptual quality of signal is poor
Reduce the sampling rate
  44kHz to 22kHz or 22kHz to 10kHz
  Again only a gain of a factor of 2 in size.
  Total loss of all high frequency information.
  Equivalent to a high pass filter.
A factor 10:1 in compression cannot be achieved using linear compression schemes

## Slide 12: Perceptual Coding
Start by evaluating input response of bitstream consumer (eg, human ears or eyes), i.e., how consumer will perceive the input.
  Frequency range, amplitude sensitivity, color response, …
  Masking effects
Identify information that can be removed from bit stream without perceived effect, e.g.,
  Sounds outside frequency range
  Masked sounds
Encode remaining information efficiently
  Use frequency-based transformations
  Quantize coefficients of frequency (loss occurs here)
  Add lossless coding (e.g. the Huffman encoding to be studied later)

## Slide 13: Principles of Auditory Coding
Time frequency decomposition
  divide the signal into frames
  obtain the spectrum of each piece
Use psycho-acoustic model to determine what information to keep
  Don’t store information outside the range of hearing (40Hz to 15kHz)
  Stereo info not stored for low frequencies
  Masking
Store the information in the most compact way possible
  minimize the bitrate
  maximize the audible auditory content

## Slide 14: Masking
If a dominant tone is present then noise can be added at frequencies next to it and this noise will not be heard.
Coding consequences
  Less precision is required to store nearby frequencies
  Less precision = coarser quantization
Definitions
  Auditory threshold – minimum signal level at which a pure tone can be heard
  Masking threshold – minimum signal level if a dominant tone is present

## Slide 15: MP3 schematic
Input: 16 bit at 44kHz sampling is 768kbit/s
Output: Coded audio signal at ~128kbit/s
Frequency analysis
similar to Fourier series
Frequency analysis
similar to Fourier series
loss of information
happens here
effects of masking
determined here
lossless compression
to be studied later
minor extra
information
encoded here

## Slide 16: Quantization
When creating a digital representation of a sampled value, we must choose the number of bits used to represent the value.
Since fewer bits encode a smaller number of values, using fewer bits results in a larger quantization error
  quantization error = difference between the actual and encoded value
  We want quantization error to be small, i.e. more bits.
On the other hand, fewer bits take up less space.
four possible
values
eight possible
values
sixteen possible
values
quantization
error

## Slide 17: Non-uniform quantization
MP3 compression quantizes the amplitudes of different frequency components differently, depending upon masking.
Frequency components near a dominant masker are quantized with lower bits.
Frequency analysis
similar to Fourier series
Frequency analysis
similar to Fourier series
loss of information
happens here
effects of masking
determined here
lossless compression
to be studied later
minor extra
information
encoded here

## Slide 18: Summary
Audio waveforms are typically analyzed as a sequence of frames
  Within each frame, the signal can be well approximated by a few frequency components
  The spectrogram can be used to visualize changes in the frequency content over time
  Framing is used in MP3 audio compression
MP3 audio compression combines framing and frequency analysis with a non-uniform quantization based on a perceptual model
  Quantization results in loss of information
  By throwing away “unimportant” (imperceptible) information, we can obtain large compression ratios.
  We will study a very simple version of this idea in the lab.